## Slide 1: CS4101 嵌入式系統概論 Embedded Real-Time OS
Prof. Chung-Ta King
Department of Computer Science
National Tsing Hua University, Taiwan
(Materials from Prof. P. Marwedel of Univ. Dortmund, Richard Barry, and
http://www.eecs.umich.edu/eecs/courses/eecs373/Lec/RTOS2.pptx)

## Slide 2: Outline
Embedded and real-time operating systems
  Embedded operating systems
  Overview of real-time systems
  Real-time operating systems (RTOS)
FreeRTOS
  Tasks
  Link to FreeRTOS on Arduino
Tasks in FreeRTOS
  Task states
  Task creation and deletion

## Slide 3: Operating Systems
The collection of software that manages a system’s hardware resources
  Often include a file system module, a GUI and other components
Often times, a “kernel” is understood to be a subset of such a collection
Characteristics
  Resource management
  Interface between application and hardware
  Library of functions for the application
  Applications are compiled separately from the OS
Notes: Resource management - e.g. memory, processor, hard disk, cd-rom, printer
Interface between application and hardware
Creation of an operating system-API for hardware - leads to a simple handling of the hardware for the programmer (minor knowledge of hardware)
Library of functions for application
Use:
The operating system has a big influence at software reliability, productivity, maintenance and service.
Allocation of resources (cpu, memory, etc) for the application
Deletion of conflict situations

## Slide 4: Embedded Operating System (EOS)
Application is compiled and linked together with the embedded OS
  On system start, application usually gets executed first, and it then starts the EOS
  Typically only part of the OS (services or functions) that are needed to support the embedded system are configured and linked in
Characteristics:
  Resource management
  Less overhead
  Code of OS and application mostly reside in ROM
(Dr Jimmy To, EIE, POLYU)
Notes: Resources management
Optimising to less memory requirement
Processor
Mostly no management of the ports and periphery (limitation to operating system kernel)
Less Overhead
Run time
Memory requirement (RAM, ROM)
Interface: Relation to the outside world (input.- and output signals)
Kind of operating system:
Single-/multi-user system
Timesharing (multi-access)
Multitasking
Batch

## Slide 5: Characteristics of Embedded OS
Embedded OS need to be configurable:
  No single OS fit all needs  install only those needed
  e.g., conditional compilation using #if and #ifdef
Device drivers often not integrated into kernel
  Embedded systems often application-specific  specific devices  move devices out of OS to tasks
Embedded OS
Standard OS
kernel

## Slide 6: Characteristics of Embedded OS
Protection is often optional
  Embedded systems are typically designed for a single purpose, untested programs rarely loaded, and thus software is considered reliable
  Privileged I/O instructions not necessary and tasks can do their own I/O, e.g., switch is address of some switch: Simply use
  load register, switch instead of OS call
Real-time capability
  Many embedded systems are real-time (RT) systems and, hence, the OS used in these systems must be real-time operating systems (RTOSs)

## Slide 7: What is a Real-Time System?
Real-time systems have been defined as: "those systems in which the correctness of the system depends not only on the logical result of the computation, but also on the time at which the results are produced"
  J. Stankovic, "Misconceptions about Real-Time Computing," IEEE Computer, 21(10), October 1988.

## Slide 8: Real-Time Characteristics
Pretty much typical embedded systems
  Sensors and actuators all controlled by a processor
  The big difference is timing constraints (deadlines)
Tasks can be broken into two categories1
  Periodic Tasks: time-driven, recurring at regular intervals
    An air monitoring system taking a sample every 10 seconds
    Flash LEDs in 1 Hz
  Aperiodic: event-driven
    The airbag of a car having to react to an impact
    Press a button
  1Sporadic tasks are sometimes considered as a third category. They are tasks similar to aperiodic tasks but activated with some known bounded rate, which is characterized by a minimum interval of time between two successive activations.

## Slide 9: Soft, Firm and Hard deadlines
The instant at which a result is needed is called a deadline
If the result has utility even after the deadline has passed, the deadline is classified as soft, otherwise it is firm
If a catastrophe could result if a firm deadline is missed, the deadline is hard

## Slide 10: Goals of an RTOS
Manage to meet RT deadlines
Also like
  Deadlines met
    Ability to specify scheduling algorithm
    Interrupts are fast
    Interrupt prioritization easy to set
  Tasks stay out of each others’ way
    Normally through page protection
  Device drivers already written (and tested!) for us
  Portable—runs on a huge variety of systems
  Nearly no overhead so we can use a small device!
    That is a small memory and CPU footprint
Notes: Tasks stay out of each others’ way: One task running awry shouldn’t take the rest of the system down.
This generally requires a lot of overhead.
  Need some sense of process number/switching
  Need some kind of MMU in hardware
Device drivers already written (and tested!) for us:
-- Ideally the RTOS has drivers for all the on-board peripherals.
-- It’s a lot easier to call a “configure_I2C()” function than to read the details of the device specification and do the memory-mapped work yourself

## Slide 11: Requirements for RTOS
Predictability of timing behavior of the OS
  Upper bound on execution time for all OS services
  Scheduling policy must be deterministic
  Period in which interrupts are disabled must be short (to avoid unpredictable delays in processing critical events)
OS should manage timing and scheduling
  OS has to be aware of task deadlines (unless scheduling is done off-line)
  OS should provide precise time services with high resolution
    Important if internal processing of the embedded system is linked to an absolute time in the physical environment

## Slide 12: Functionality of RTOS Kernel
Processor management
Memory management
Timer management
Task management (resume, wait, etc.)
Inter-task communication
Task synchronization
resource management

## Slide 13: Outline
Embedded and real-time operating systems
  Embedded operating systems
  Overview of real-time systems
  Real-time operating systems (RTOS)
FreeRTOS
  Tasks
  Link to FreeRTOS on Arduino
Tasks in FreeRTOS
  Task states
  Task creation and deletion

## Slide 14: FreeRTOS
FreeRTOS is nothing but software that provides multitasking facilities
  Allows to run multiple tasks and has a simple scheduler to switch between tasks (priority-based multitasking)
    Fully preemptive
    Always runs the highest priority task that is ready to run
    Context switch occurs if a task/co-routine blocks or a task/co-routine yields the CPU
  Queues to communicate between multiple tasks
  Semaphores for resource sharing between multiple tasks
  Utilities to view CPU utilization, stack utilization etc.
(http://www.socialledge.com/sjsu/index.php?title=FreeRTOS_Tutorial)

## Slide 15: Ticks
System runs on “ticks”
  Every tick the kernel runs and figures out what to do next.
    Interrupts have a different mechanism
  Basically a hardware timer is set to generate regular interrupts for ticks and calls the scheduler.
    This means the OS occupies one of the timers—you can’t easily share.

## Slide 16: Tasks in FreeRTOS
In FreeRTOS, computations are organized around tasks, which are the most basic unit of scheduling
  A task is a thread
A task is a function that must return void and take a void pointer parameter:
  void ATaskFunction(void *pvParameters);
  A task normally runs in an infinite loop and must not return
You inform the scheduler of
  The task’s resource needs (stack space, priority)
  Any arguments the task needs

## Slide 17: Example: Creating a Task
void setup() {
// Now set up two tasks to run independently
xTaskCreate(
vTask1, // Pointer to function for the task
(const portCHAR *) "Task1", // Name for the task
128, // Stack size
NULL, // NULL task parameter
1, // This task will run at priority 1
NULL ); // Do not use the task handle
xTaskCreate(vTask2, "Task2", 1000, NULL, 1, NULL);
/* Now the task scheduler, which takes over control of scheduling individual tasks, is automatically started */
}
void loop() {
// Empty! Things are done in Tasks.
}

## Slide 18: Example: Creating a Task
void vTask1(void *pvParameters) {
(void) pvParameters;
for( ;; ) // A Task shall never return or exit.
{
// do whatever the task is to do
}
}
void vTask2(void *pvParameters) {
(void) pvParameters;
for( ;; ) // A Task shall never return or exit.
{
// do whatever the task is to do
}
}

## Slide 19: Link to FreeRTOS on Arduino
There is a FreeRTOS implementation in Arduino IDE
  Go to “Sketch”  “Include Library”  “Manage Libraries…” to open Arduino IDE Library manager

## Slide 20: Link to FreeRTOS on Arduino
In the Arduino IDE Library manager (from Arduino Version 1.8.4) look for the FreeRTOS Library
  Type: “Contributed” and Topic: “Timing”

## Slide 21: Link to FreeRTOS on Arduino
Under the “Sketch”  “Include Library”, ensure that the FreeRTOS library is included in your sketch

## Slide 22: Example: Blink_AnalogRead
#include <Arduino_FreeRTOS.h>
/* define two tasks for Blink & AnalogRead */
void TaskBlink(void *pvParameters);
void TaskAnalogRead(void *pvParameters);
void setup() {
Serial.begin(9600);
while (!Serial) {
; // wait for serial port to connect.
}
/* Now set up two tasks to run independently */
xTaskCreate(TaskBlink, (const portCHAR *)"Blink", 128,
NULL, 2, NULL);
xTaskCreate(TaskAnalogRead,
(const portCHAR *) "AnalogRead", 128, NULL, 1,
NULL);
}

## Slide 23: Example: Blink_AnalogRead
void loop() {
// Empty. Things are done in Tasks.
}
void TaskBlink(void *pvParameters) {
(void) pvParameters;
pinMode(LED_BUILTIN, OUTPUT);
for (;;) { // A Task shall never return or exit.
digitalWrite(LED_BUILTIN, HIGH); // turn on the LED
vTaskDelay(1000); // wait for 1000 ticks
digitalWrite(LED_BUILTIN, LOW); // turn off the LED
vTaskDelay(1000); // wait for 1000 ticks
}
}

## Slide 24: Example: Blink_AnalogRead
void TaskAnalogRead(void *pvParameters) {
(void) pvParameters;
for (;;) {
/* read the input on analog pin 0 */
int sensorValue = analogRead(A0);
/* print out the value you read */
Serial.println(sensorValue);
/* one tick delay in between reads for stability */
vTaskDelay(1);
}
}

## Slide 25: Outline
Embedded and real-time operating systems
  Embedded operating systems
  Overview of real-time systems
  Real-time operating systems (RTOS)
FreeRTOS
  Tasks
  Link to FreeRTOS on Arduino
Tasks in FreeRTOS
  Task states
  Task creation and deletion

## Slide 26: Task States in FreeRTOS
Running:
  Task is actually executing
  Only one task can exist in Running state at any one time (assuming 1-core system)
Ready:
  Task is ready to execute but a task of equal or higher priority is Running

## Slide 27: Task States in FreeRTOS
Blocked:
  Task is waiting for some event
    Time: if a task calls vTaskDelay() it will be blocked until the delay period has expired
    Resource: tasks can also block waiting for queue and semaphore events
Suspended:
  Much like blocked, but not waiting for anything
  Tasks will only enter or exit the suspended state when explicitly commanded to do so through the vTaskSuspend() and vTaskResume() API calls respectively

## Slide 28: Task Creation
xTaskCreate(pvTaskCode, pcName, usStackDepth, pvParameters, uxPriority, pxCreatedTask)
  pvTaskCode: pointer to task entry function, implemented to never return
  pcName: a descriptive name for the task to facilitate debugging
  usStackDepth: size of task stack, specified as the number of variables that the stack can hold
  pvParameters: pointer to parameters for the task
  uxPriority: priority at which the task should run; low numeric priority values denote low priority
  pvCreatedTask: pass back a handle to reference the task

## Slide 29: Task Deletion
A created task commonly runs in an infinite loop, but it may be deleted by
void vTaskDelete(TaskHandle_t xTask);
  xTask: handle of the task to be deleted; NULL to cause the calling task to be deleted
  Remove a task from the RTOS kernels management
void vOtherFunction(void) {
TaskHandle_t xHandle = NULL;
// Create the task, storing the handle.
xTaskCreate(vTaskCode, "NAME", STACK_SIZE, NULL,
tskIDLE_PRIORITY, &xHandle);
// Use the handle to delete the task.
if(xHandle != NULL) vTaskDelete(xHandle);
}
Notes: Memory allocated by the task code is not automatically freed, and should be freed before the task is deleted.