## Slide 1: CS4101 Introduction to Embedded Systems Lab 11: Task Communication
Prof. Chung-Ta King
Department of Computer Science
National Tsing Hua University, Taiwan

## Slide 2: Lab 11
Basic 1: Moving Control (30%)
  Connect LCD and Keypad to your Arduino UNO.
  Use the Keypad to move a character on LCD.
    Use button “2” for up, ”8” for down, “4” for left, “6” for right.
    Initialize the character on position (0,0).
    You should avoid the character from running out of the edge.
  Create two tasks, “controlTask” and “displayTask”.
    controlTask: Read inputs from Keypad, calculate position of the character, inform displayTask of the position through a queue. No LCD-printing, but serial printing is allowed.
    displayTask: Receive position information from the queue and display the character. No calculation in this task.

## Slide 3: Lab 11
Basic 1: Moving Control (40%)
  Constraints:
    Only variables used by the I/O modules could be declared as global. Any other global variables are not allowed.  Use only queue to communicate between the two tasks.
    Only one queue is allowed.
  The character:
    Yon can print any thing you want, but not larger than one cell (5x8 pixel). Or you can use the “byte err_dragon[8]” symbol on the next slide.
    How do lcd.createChar() and lcd.write() work?
      https://www.arduino.cc/en/Reference/LiquidCrystalCreateChar

## Slide 4: lcd.createChar() and lcd.write()
#include <Arduino_FreeRTOS.h> #include <Key.h> #include <Keypad.h> #include <LiquidCrystal_I2C.h> LiquidCrystal_I2C lcd(0x27,16,2); byte err_dragon[8] = {B00111, B00101, B00110, B00111, B10100, B10111, B01110, B01010}; void setup(){ Serial.begin(9600); lcd.init(); lcd.backlight(); lcd.createChar(0, minesweeper); } void loop(){ lcd.setCursor(0,0); lcd.write(0); }

## Slide 5: Lab 11
Basic 2: Minesweeper (60%)
  Extension of Basic 1 and having same constraints.
  Start of the game:
    A mine is placed randomly on the field of size 2*16.
    The minesweeper is initialized on cell (0,0).
    The minesweeper has 10 mine-removers.
    All cells are covered with the “unchecked” character.
  Game rules: find the mine and clear it.
    Move the minesweeper as in Basic 1.
    When the minesweeper reaches a cell, it can either apply 1 mine-remover to try to remove the mine or it just moves on to the next cell and does nothing.
    Press button “5” to apply a mine-remover.

## Slide 6: Lab 11
Basic 2: Minesweeper (cont.)
  Game rules: (cont.)
    If minesweeper just passes by a cell and does nothing, if the mine is on the cell, minesweeper explodes  show “exploded” character for 1 sec, start new game. else still mark the position as “unchecked”.
    If button “5” is pressed, deduct 1 mine-remover. if the mine is on the cell, show “succeeded” character for 1 sec, start new game; else show “1” if mine is within 3 cells from current cell, otherwise show “0”. After showing 1 or 0 for 1 sec, show minesweeper again. When minesweeper leaves the cell, show 1 or 0 again.

## Slide 7: Lab 11
Basic 2: Minesweeper (cont.)
  Game rules: (cont.)
    If mine-removers become 0, then game over and start a new game.
  Implementation:
    Follow same constraints as Basic 1.
    Add a task “mapTask”: Initialize the game. Only runs on the start of the game.
    Can use more than one queue. But beware the number and the size of your queues.

## Slide 8
byte minesweeper[8] = {B01110, B01110, B10100, B11111, B00101, B01110, B01010, B11011}; byte unchecked[8] = {B11111, B11111, B11111, B11111, B11111, B11111, B11111, B11111}; byte exploded[8] = {B00100, B10101, B01110, B11111, B11111, B01110, B10101, B00100}; byte succeeded[8] = {B00100, B00110, B00111, B00110, B00100, B00100, B01110, B11111};

## Slide 9: Lab 11
Basic 2: Minesweeper (cont.)
  Demo:
  Should be like this :
  https://drive.google.com/open?id=1IFaaz1_rJjSZeMpKNaSMWawQrY9qOWKg
  Showing the mine with “X” (but please do not follow this video) :
  https://drive.google.com/open?id=1LoO-Ti7Oz1-ftSQM4h9zHbr6HxTRA399